## Slide 1
Coalition for Eco-Efficient Comminution

## Slide 2: Session 1
The energy challenge for comminution
Key aspects of the challenge
Total energy – direct and indirect
Opportunities to improve energy efficiency in comminution
  Mine to mill and beyond (integrating blasting)
  Upgrading ore, Coarse recovery, Sorting
  Multiple process streams

## Slide 3: Some key challenges
Michaux 2011

## Slide 4: Energy
Energy comes at great cost to our world and societies
We should use it wisely and optimally
Society pressure is enforcing this
We need to be proactive

## Slide 5: Energy use
Stage | Feed, mm | Prod, mm | Energy, %
Mining | >1000 | <300 | 1
Crushing | 300 | 20 | 10
Milling | 20 | 0.1 | 89
 |  | subtotal | 100
Fine grinding | 0.1 | 0.008 | 100

## Slide 6: Energy Efficiency
We use >3 times energy in a mill
relative to single particle breakage
Mills 30 – 40% efficient
60 – 70%
Opportunity

## Slide 7: Energy Saving Opportunities

## Slide 8
Energy Saving Opportunity in U.S. Mining Industry (Mining Process Equipment)
Source: Mining Energy Bandwidth Study (Draft 2007)

## Slide 9
BCS, June 2007. Mining industry energy bandwidth study. US Department of energy

## Slide 10: Reduction in Energy use
6-7% Australia’s energy on comminution
Mining houses target of 10-20% reduction
But:
  Drop in grade + increase in hardness
Need to reduce kWh/t of ore to 40% of existing levels !
Is this achievable?!

## Slide 11: Energy Accounting
Forced accounting of Carbon Footprint of Steel :
infrastructure of plant construction
consumables in mining process
  –Balls in mills
  –In large mines, can be as much as ¼ million tonnes per annum in ball consumption

## Slide 12: Total Energy

## Slide 13: Accounting for embodied energy
A more sustainable approach to assessing comminution
Efficiency, Fiesal Musa and Rob Morrison, 2008
GHG =